## Slide 1: Computer Networks
Lecture 7: Data Link layer
Based on slides from D. Choffnes Northeastern U. and P. Gill from StonyBrook University
Revised Autumn 2015 by S. Laki

## Slide 2: Cyclic Redundancy Check (CRC)
Uses field theory to compute a semi-unique value for a given message
Much better performance than previous approaches
  Fixed size overhead per frame (usually 32-bits)
  Quick to implement in hardware
  Only 1 in 232 chance of missing an error with 32-bit CRC

## Slide 3: CRC (Cyclic Redundancy Check)
Polynomial code
  Treating bit strings as representations of polynomials with coefficients of 0 and 1.
CRC
  Add k bits of redundant data to an n-bit message.
  Represent n-bit message as an n-1 degree polynomial;
    e.g., MSG=10011010 corresponds to M(x) = x7+ x4 + x3 + x1.
  Let k be the degree of some divisor polynomial G(x);
    e.g., G(x) = x3+ x2 + 1.
    Generator polynomial
      Agreed upon it in advance

## Slide 4: CRC
Transmit polynomial P(x) that is evenly divisible by G(x), and receive polynomial P(x) + E(x);
  E(x)=0 implies no errors.
Recipient divides (P(x) + E(x)) by G(x);
  the remainder will be zero in only two cases:
    E(x) was zero (i.e. there was no error),
    or E(x) is exactly divisible by C(x).
Choose G(x) to make second case extremely rare.

## Slide 5: A basic example with numbers
Make all legal messages divisible by 3
If you want to send 10
  First multiply by 4 to get 40
  Now add 2 to make it divisible by 3 = 42
When the data is received ..
  Divide by 3, if there is no remainder there is no error
  If no error, divide by 4 to get sent message
If we receive 43, 44, 41, 40, then error
45 would not be recognized as an error

## Slide 6: Mod 2 arithmetic
Operations are done modulo 2
1111
+1010
=====
0101
11001
x 101
=====
11001
+ 11001
=========
1111101

## Slide 7: A basic example with polynomials
Sender:
  multiply M(x) = x7+ x4 + x3 + x1 by xk; for our example, we get
    x10 + x7 + x6 + x4 (10011010000);
  divide result by C(x) (1101);
  Send 10011010000 + 101 = 10011010101,
  since this must be exactly divisible by C(x);
11111001
10011010000 Message
1101
1001
1101
1000
1101
1011
1101
1100
1101
1000
1101
101 Remainder
Generator 1101

## Slide 8: Further properties
Want to ensure that G(x) does not divide evenly into polynomial E(x).
All single-bit errors, as long as the xk and x0 terms have non-zero coefficients.
All double-bit errors, as long as G(x) has a factor with at least three terms.
Any odd number of errors, as long as G(x) contains the factor (x + 1).
Any “burst” error (i.e sequence of consecutive errored bits) for which the length of the burst is less than k bits.
Most burst errors of larger than k bits can also be detected.

## Slide 9: Even Parity
Actually consists of using x+1 polynomial
Given message 0111, multiply by x to get 01110
Now divide by x+1=11
11 01110
11
0010
11
1=remainder
Message = 01110+1=01111 even parity
0101

## Slide 10
Common polynomials for C(x):
CRC
CRC-8
CRC-10
CRC-12
CRC-16
CRC-CCITT
CRC-32
C(x)
x8+x2+x1+1
x10+x9+x5+x4+x1+1
x12+x11+x3+x2+x1+1
x16+x15+x2+1
x16+x12+x5+1
x32+x26+x23+x22+x16+x12+x11+x10+x8+x7+x5+x4+x2+x+1

## Slide 11: Error control
Error Control Strategies
  Error Correcting codes (Forward Error Correction (FEC))
  Error detection and retransmission Automatic Repeat Request (ARQ)

## Slide 12: Error control
Objectives
  Error detection
    with correction
      Forward error correction
    without correction -> e.g. drop a frame
      Backward error correction
      The erroneous frame needs to be retransmitted
  Error correction
    without error detection
      e.g. in voice transmission

## Slide 13: Should We Error Check in the Data Link?
Recall the End-to-End Argument
Cons:
  Error free transmission cannot be guaranteed
  Not all applications want this functionality
  Error checking adds CPU and packet size overhead
  Error recovery requires buffering
Pros:
  Potentially better performance than app-level error checking
Data link error checking in practice
  Most useful over lossy links
  Wifi, cellular, satellite

## Slide 14: Backward Error Correction

## Slide 15: Backward error correction
Network Layer
Data Link Layer
Physical Layer
Network Layer
Data Link Layer
from_upper(p)
to_lower(p)
to_upper(p)
from_lower(p)
Packets
Frames
Bits
Error detection at the receiver side
The sender retransmits a frame until it received by the other side correctly.

## Slide 16: Model of Frame Transmission

## Slide 17: Elementary Data Link Protocols
Simplex Stop-and-Wait Protocol
Alternate Bit Protocol
Sliding Window Protocol

## Slide 18: Simple Stop-and-Wait Protocol
A sends a message to B
A stops and waits for an answer from B
  Acknowledgement message (ACK)
After receiving the message B sends an ACK back to the sender.
A retransmits the message until it receives an ACK from B
If the ACK arrived, the next message may be sent.

## Slide 19: Simplex Stop-and-Wait Protocol
Sender
Receiver

## Slide 20: Stop-and-Wait Link Utilization

## Slide 21: Stop-and-Wait Diagram
Simple, but inefficient for long distance and high speed applications.
We can use sliding-window technique to improve the efficiency.

## Slide 22: What’s the problem?
Usually
Packet loss
ACK loss

## Slide 23: Alternating Bit Protocol (ABP)
Let
  A be the sender
  B be the receiver
A and B maintain internal one-bit counter
  A value that is 0 or 1
Each message from A to B contains
  a data part and
  a one-bit sequence number
    E.g. a value that is 0 or 1
After receiving A’s message, B sends an ACK back to A
  which also contains a one-bit sequence number
Retransmission until A receives an ACK from B with the same sequence number
  Then A complements its sequence number
    0->1 or
    1->0

## Slide 24: Alternating Bit Protocol (ABP)
Sender
Receiver

## Slide 25: Alternating Bit Protocol (ABP)
A reliable data transport over a noisy channel
Basic flow control
  The sender has to wait for the ACK from the receiver before sending the next message
Automatic Repeat reQest (ARQ) protocol
An acknowledgement
  marks that the new message has been delivered.
  allows the sender to tranmit the next frame.

## Slide 26: Alternating Bit Protocol
Two scenarios for ABP. (a) Normal case. (b) Abnormal case. The notation is (seq, ack, packet number). An asterisk indicates where a network layer accepts a packet.

## Slide 27: ABP – Channel utilization
Utilization (η) is the ratio of
  The time needed for the transmission of a frame (Tpacket)
  The time ellapsed until the next frame can be transmitted
    In the fig.: (Tpacket + d + Tack + d)
Now:
  η = Tpacket / (Tpacket + d + Tack + d)
If the propagation delay is large, the ABP is not efficient.
Time

## Slide 28: How to improve the efficency?
The sender transmit frames continously one after another
  More frames are sent out, but not acknowledged.
  Pipeline technique
Introduce sequence numbers
Time

## Slide 29: Sliding Window Protocols
Similar to ABP
but allow multiple frames to transmit
  Receiver has a buffer of W frames
  Sender can send up to W frames without receiving ACK
Bidirectional
Each outgoing frame contains a seq. number from 0 to 2n-1.
  So it fits in an n-bit field
  ABP uses n=1
Each ACK carries the sequence number of the next expected frame by the receiver

## Slide 30: Sliding Window Protocols
At the sender
  Sending window
    a set of sequence numbers corresponding to frames being under transmission (finite range of numbers)
At the receiver
  Receiving window
    Sequence numbers for frames it is permitted to accept (finite range of numbers)
The sender’s and receiver’s windows need
  not have tha same lower and upper bounds and
  even have the same size.
The window size can be
  fixed or
  grow or shrink over the course of time as frames are sent and received

## Slide 31: Sliding-Window Diagram
Need to buffer them in case of retransmission
Notes: Assume 3-bit sequence number is used. Frames are numbered sequentially from 0 through 7.
In Fig.(a), each time a frame is sent, the shaded window shrinks; each time an ACK is received, the shaded window grows.

## Slide 32: Example Sliding-Window
RR3 means the receiver has received all frames up to frame 2 and is ready to receive frame 3.
Have been delivered to upper layer
More spaces for future frames
Notes: It is not necessary to acknowledge every frame.

## Slide 33: Sliding Window Protocols
A sliding window of size 1, with a 3-bit sequence number.
(a) Initially.
(b) After the first frame has been sent.
(c) After the first frame has been received.
(d) After the first acknowledgement has been received.

## Slide 34: Go-Back-N
A sliding window protocol where
  the receiver’s window size is fixed to 1,
  while the sender has window size > 0.
After receiving a damaged frame
  Receiver discards all subsequent frames
  Sender retransmits the damaged frame and all its successors after the times out

## Slide 35: Go-Back-N

## Slide 36: Selective Repeat
Receiver’s window size is n ( n >1 )
  At most n frames can be buffered
Receiver stores all the correct frames following the bad one
The sender retransmits only the bad frame not all its successors

## Slide 37: Selective Repeat

## Slide 38: Communication channels and piggybacking
Simplex
  Communication in one direction only
Half-duplex
  Communication in both directions, but only one direction at a time, not simultaneously.
Full-duplex
  Communication in both directions simultaneously
The previous protocols assumed
  a simplex channel to the upper (network) layer and
  a (half-)duplex channel to the physical layer
If we use duplex channel to the upper layers
  Transmitting data packet and acknowledgements in both directions separately
  Or using piggybacking
    The header of a data packet sent in the opposite direction carries the acknowledgement back to the other side
    widely applied in practice

## Slide 39: Ethernet frame

## Slide 40: Outline
Framing
Error Checking and Reliability
Media Access Control
  802.3 Ethernet
  802.11 Wifi

## Slide 41: What is Media Access?
Ethernet and Wifi are both multi-access technologies
  Broadcast medium, shared by many hosts
  Simultaneous transmissions cause collisions
    This destroys the data
Media Access Control (MAC) protocols are required
  Rules on how to share the medium
  Strategies for detecting, avoiding, and recovering from collisions

## Slide 42: Strategies for Media Access
Channel partitioning
  Divide the resource into small pieces
  Allocate each piece to one host
  Example: Time Division Multi-Access (TDMA) cellular
  Example: Frequency Division Multi-Access (FDMA) cellular
Taking turns
  Tightly coordinate shared access to avoid collisions
  Example: Token ring networks

## Slide 43: Channel Partitioning
Frequency Division Multiplexing
  E.g. a telephone trunk
Time Division Multiplexing
Are they good solutions?
  if data rates are fixed
  if the link utilization is good

## Slide 44: What’s the problem?
The number of senders is large
continuously varying
bursty traffic

## Slide 45: Bursty traffic
If there’s huge difference between the peak rate and the mean (or average) rate
In computer networks it is not rare
  peak rate/mean rate = 1000/1

## Slide 46: Bursty traffic with Static Channel Allocation
The capacity of the channels must be
  Either quite large to handle peak rates
    Waste of resources
    The mean rate is much less than the peak one
  Or based on the mean rate
    We need buffers/queues to store packets coming faster than the mean rate
    Queuing delays
BUFFERS
Incoming packets

## Slide 47: What’s about delays?
If there’s no multiplexing
  A source has data rate of p bps
  The capacity of the link is C bps
  The delay is T
Bursty traffic with static channel allocation
  Dividing the channel into N static subchannels
    With sending rate p/N bps and capacity C/N
  The delay is N T
Static channel allocation increases the packet delays
Because of the idle subchannels

## Slide 48: Dynamic Channel Allocation in LANs and MANs
1. Station Model.
  N terminals/hosts
  The prob. of a frame being generated in Δt is λΔt, where the arrival rate is λ.
2. Single Channel Assumption.
  All stations are equivalent
  A single channel is available for all communications
3. Collision Assumption.
  If two frames are transmitted simultaneously, they overlap in time which results a garbled signal
  This event is called collision
4. Continuous Time VS Slotted Time.
5. Carrier Sense VS No Carrier Sense.

## Slide 49: Dynamic Channel Allocation in LANs and MANs
4. Continuous Time VS Slotted Time.
5. Carrier Sense VS No Carrier Sense.
Time
Time

## Slide 50: How can the efficiency be measured?
Throughput (S)
  Number of packets/frames transmitted in a time unit (successfully)
Delay
  The time needs for transmitting a packet
Fairness
  All the terminals are treated as equals

## Slide 51: Throughput and offered load
Offered load (G)
  The number of packets in a time unit that the protocol must handle
  G>1: overloading
An ideal protocol
  If G<1, S=G
  If G≥1, S=1
  where sending out a packet takes 1 time unit.

## Slide 52: Strategies for Media Access
Channel partitioning
  Divide the resource into small pieces
  Allocate each piece to one host
  Example: Time Division Multi-Access (TDMA) cellular
  Example: Frequency Division Multi-Access (FDMA) cellular
Taking turns
  Tightly coordinate shared access to avoid collisions
  Example: Token ring networks
Contention
  Allow collisions, but use strategies to recover
  Examples: Ethernet, Wifi

## Slide 53: Contention MAC Goals
Share the medium
  Two hosts sending at the same time collide, thus causing interference
  If no host sends, channel is idle
  Thus, want one user sending at any given time
High utilization
  TDMA is low utilization
  Just like a circuit switched network
Simple, distributed algorithm
  Multiple hosts that cannot directly coordinate
  No fancy (complicated) token-passing schemes

## Slide 54: Contention Protocol Evolution
ALOHA
  Developed in the 70’s for packet radio networks
  Stations transmit data immedately
    If there is a collision, it retransmits the packet later.
Slotted ALOHA
  Start transmissions only at fixed time slots
  Significantly fewer collisions than ALOHA
Carrier Sense Multiple Access (CSMA)
  Start transmission only if the channel is idle
CSMA / Collision Detection (CSMA/CD)
  Stop ongoing transmission if collision is detected
Notes: ALOHA:
Send data if you have data (doesn’t bother sensing the medium)
Later  back off period e.g., exponential backofff etc.

## Slide 55: Pure ALOHA
The goal was to use low-cost commercial radio equipment to connect users on Oahu and the other Hawaiian islands with a central time-sharing computer on the main Oahu campus.
Algorithm was developed by Uni. of Hawaii
  If you have data to send, send the data
  Low-cost and very simple

## Slide 56: ALOHA
Topology: radio broadcast with multiple stations
Protocol:
  Stations transmit data immediately
  Receivers ACK all packets
  No ACK = collision, wait a random time then retransmit
A
B
C
Simple, but radical concept
Previous attempts all divided the channel
  TDMA, FDMA, etc.
Optimized for the common case: few senders

## Slide 57: Performance analysis -Poisson Process
The Poisson Process is a celebrated model used in Queuing Theory for “random arrivals”. Assumptions leading to this model include:
  The probability of an arrival during a short time interval Δt is proportional to the length of the interval, and does not depend on the origin of the time interval (memory-less property)
  The probability of having multiple arrivals during a short time interval Δt approaches zero.

## Slide 58: Performance analysis - Poisson Distribution
The probability of having k arrivals during a time interval of length t is given by:
where λ is the arrival rate. Note that this is a single-parameter model; all we have to know is λ.

## Slide 59: FYI: Poisson Distribution
The following is the plot of the Poisson probability density function for four values of λ.

## Slide 60: Analysis of Pure ALOHA
Notation:
  Tf = frame time (processing, transmission, propagation)
  S: Average number of successful transmissions per Tf ; that is, the throughput
  G: Average number of total frames transmitted per Tf
  D: Average delay between the time a packet is ready for transmission and the completion of successful transmission.
We will make the following assumptions
  All frames are of constant length
  The channel is noise-free; the errors are only due to collisions.
  Frames do not queue at individual stations
  The channel acts as a Poisson process.

## Slide 61: Analysis of Pure ALOHA…
Since S represents the number of “good” transmissions per frame time, and G represents the total number of attempted transmissions per frame time, then we have:
S = G ´ (Probability of good transmission)
The vulnerable time for a successful transmission is 2Tf
So, the probability of good transmission is not to have an “arrival” during the vulnerable time .

## Slide 62: Analysis of Pure ALOHA…
t0
t0 + t
t0 + 2t
t0 + 3t
Collides with
the start of
the shaded
frame
Collides with
the end of
the shaded
frame
Vulnerable
Time
Vulnerable period for the shaded frame
t
Notes: 2

## Slide 63: Analysis of Pure ALOHA…
Using:
And setting t = 2Tf and k = 0, we get

## Slide 64: Analysis of Pure ALOHA…
If we differentiate S = Ge-2G with respect to G and set the result to 0 and solve for G, we find that the maximum occurs when
G = 0.5,
and for that S = 1/2e = 0.18. So, the maximum throughput is only 18% of capacity.
Notes: 2

## Slide 65: Tradeoffs vs. TDMA
In TDMA, each host must wait for its turn
  Delay is proportional to number of hosts
In Aloha, each host sends immediately
  Much lower delay
  But, much lower utilization
ALOHA Frame
ALOHA Frame
Time
Sender A
Sender B
  Maximum throughput is ~18% of channel capacity
Load
Throughput

## Slide 66: Slotted ALOHA
Channel is organized into uniform slots whose size equals the frame transmission time.
Transmission is permitted only to begin at a slot boundary.
Here is the procedure:
  While there is a new frame A to send do
Send frame A at (the next) slot boundary
Notes: 2

## Slide 67: Analysis of Slotted ALOHA
Note that the vulnerable period is now reduced in half. Using:
And setting t = Tf and k = 0, we get

## Slide 68: Slotted ALOHA
Protocol
  Same as ALOHA, except time is divided into slots
  Hosts may only transmit at the beginning of a slot
Thus, frames either collide completely, or not at all
  37% throughput vs. 18% for ALOHA
  But, hosts must have synchronized clocks
Load
Throughput

## Slide 69: 802.3 Ethernet
Preamble is 7 bytes of 10101010. Why?
Start Frame (SF) is 10101011
Source and destination are MAC addresses
  E.g. 00:45:A5:F3:25:0C
  Broadcast: FF:FF:FF:FF:FF:FF
Minimum packet length of 64 bytes, hence the pad
Preamble
SF
Source
Dest.
Length
7
1
6
6
2
Bytes
Data
Checksum
Pad
0-1500
0-46
4
Notes: 7 bytes  allows hosts on the network to

## Slide 70: Broadcast Ethernet
Originally, Ethernet was a broadcast technology
Tee Connector
Terminator
Hub
Hubs and repeaters are layer-1 devices, i.e. physical only
10Base2
10BaseT and 100BaseT
T stands for Twisted Pair
Repeater

## Slide 71: Carrier Sense Multiple Access (CSMA)
Additional assumption:
  Each station is capable of sensing the medium to determine if another transmission is underway

## Slide 72: Non-persistent CSMA
While there is a new frame A to send
  Check the medium
  If the medium is busy, wait some time, and go to 1.
  (medium idle) Send frame A

## Slide 73: 1-persistent CSMA
While there is a new frame A to send
  Check the medium
  If the medium is busy, go to 1.
  (medium idle) Send frame A

## Slide 74: p-persistent CSMA
While there is a new frame A to send
  Check the medium
  If the medium is busy, go to 1.
  (medium idle) With probability p send frame A, and probability (1- p) delay one time slot and go to 1.

## Slide 75: CSMA Summary
Non-persistent:
Transmit if idle
Otherwise, delay, try again
Constant or variable
Delay
Channel busy
Ready
1-persistent:
Transmit as soon as
channel goes idle
If collision, back off and try again
Time
p-persistent:
Transmit as soon as channel goes
idle with probability p
Otherwise, delay one slot, repeat process
CSMA persistence and backoff
Nonpersistent
1-persistent
p-persistent
Notes: 2

## Slide 76: Persistent and Non-persistent CSMA
Comparison of throughput versus load for various random access protocols.

## Slide 77: CSMA with Collision Detection
Stations can sense the medium while transmitting
A station aborts its transmission if it senses another transmission is also happening (that is, it detects collision)
Question: When can a station be sure that it has seized the channel?
  Minimum time to detect collision is the time it takes for a signal to traverse between two farthest apart stations.

## Slide 78: CSMA/CD
A station is said to seize the channel if all the other stations become aware of its transmission.
There has to be a lower bound on the length of each frame for the collision detection feature to work out.
Ethernet uses CSMA/CD

## Slide 79: CSMA/CD
Carrier sense multiple access with collision detection
Key insight: wired protocol allows us to sense the medium
Algorithm
  Sense for carrier
  If carrier is present, wait for it to end
    Sending would cause a collision and waste time
  Send a frame and sense for collision
  If no collision, then frame has been delivered
  If collision, abort immediately
    Why keep sending if the frame is already corrupted?
  Perform exponential backoff then retransmit

## Slide 80: CSMA/CD Collisions
A
B
C
D
Time
t0
t1
Detect Collision and Abort
Collisions can occur
Collisions are quickly detected and aborted
Note the role of distance, propagation delay, and frame length
Spatial Layout of Hosts

## Slide 81: Exponential Backoff
When a sender detects a collision, send “jam signal”
  Make sure all hosts are aware of collision
  Jam signal is 32 bits long (plus header overhead)
Exponential backoff operates:
  Select k ∈ [0, 2n – 1] unif. rnd., where n = number of collisions
  Wait k time units (packet times) before retransmission
  n is capped at 10, frame dropped after 16 collisions
Backoff time is divided into contention slots
Remember this number

## Slide 82: Minimum Packet Sizes
Why is the minimum packet size 64 bytes?
  To give hosts enough time to detect collisions
What is the relationship between packet size and cable length?
Propagation Delay (d)
  Time t: Host A starts transmitting
  Time t + d: Host B starts transmitting
  Time t + 2*d: collision detected
A
B
Basic idea: Host A must be transmitting at time 2*d!

## Slide 83: CSMA/CD
CSMA/CD can be in one of three states: contention, transmission, or idle.
To detect all the collisions we need
  Tf ≥ 2Tpg
  where Tf is the time needed to send the frame
  And Tpg is the propagation delay between A and B

## Slide 84: Minimum Packet Size
Host A must be transmitting after 2*d time units
  Min_pkt = rate (b/s) * 2 * d (s)
    … but what is d? propagation delay: limited by speed of light
    Propagation delay (d) = distance (m) / speed of light (m/s)
  This gives:
  Min_pkt = rate (b/s) * 2 * dist (m) / speed of light (m/s)
So cable length is equal ….
  Dist = min_pkt * light speed /(2 * rate)
10 Mbps Ethernet
Packet and cable lengths change for faster Ethernet standards
(64B*8)*(2.5*108mps)/(2*107bps) = 6400 meters

## Slide 85: Cable Length Examples
min_frame_size*light_speed/(2*bandwidth) = max_cable_length
(64B*8)*(2.5*108mps)/(2*10Mbps) = 6400 meters
What is the max cable length if min packet size were changed to 1024 bytes?
  102.4 kilometers
What is max cable length if bandwidth were changed to 1 Gbps ?
  64 meters
What if you changed min packet size to 1024 bytes and bandwidth to 1 Gbps?
  1024 meters

## Slide 86: Maximum Packet Size
Maximum Transmission Unit (MTU): 1500 bytes
Pros:
  Bit errors in long packets incur significant recovery penalty
Cons:
  More bytes wasted on header information
  Higher per packet processing overhead
Datacenters shifting towards Jumbo Frames
  9000 bytes per packet

## Slide 87: Long Live Ethernet
Today’s Ethernet is switched
  More on this later
1Gbit and 10Gbit Ethernet now common
  100Gbit on the way
  Uses same old packet header
  Full duplex (send and receive at the same time)
  Auto negotiating (backwards compatibility)
  Can also carry power