## Slide 1: Computer Networks
Lecture 10: Transport layer Part II
Based on slides from D. Choffnes Northeastern U. and P. Gill from StonyBrook University
Revised Autumn 2015 by S. Laki

## Slide 2: Transport Layer
Function:
  Demultiplexing of data streams
Optional functions:
  Creating long lived connections
  Reliable, in-order packet delivery
  Error detection
  Flow and congestion control
Key challenges:
  Detecting and responding to congestion
  Balancing fairness against high utilization
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3: TCP Congestion Control
The network is congested if the load in the network is higher than its capacity.
Each TCP connection has a window
  Controls the number of unACKed packets
Sending rate is ~ window/RTT
Idea: vary the window size to control the send rate
Introduce a congestion window at the sender
  Congestion control is sender-side problem

## Slide 4: Two Basic Components
Detect congestion
  Packet dropping is most reliably signal
    Delay-based methods are hard and risky
  How do you detect packet drops? ACKs
    Timeout after not receiving an ACK
    Several duplicate ACKs in a row (ignore for now)
Rate adjustment algorithm
  Modify cwnd
  Probe for bandwidth
  Responding to congestion

## Slide 5: Rate Adjustment
Recall: TCP is ACK clocked
  Congestion = delay = long wait between ACKs
  No congestion = low delay = ACKs arrive quickly
Basic algorithm
  Upon receipt of ACK: increase cwnd
    Data was delivered, perhaps we can send faster
    cwnd growth is proportional to RTT
  On loss: decrease cwnd
    Data is being lost, there must be congestion
Question: increase/decrease functions to use? !!!!

## Slide 6: Implementing Congestion Control
Maintains three variables:
  cwnd: congestion window
  adv_wnd: receiver advertised window
  ssthresh: threshold size (used to update cwnd)
For sending, use: wnd = min(cwnd, adv_wnd)
Two phases of congestion control
  Slow start (cwnd < ssthresh)
    Probe for bottleneck bandwidth
  Congestion avoidance (cwnd >= ssthresh)
    AIMD
Notes: Got to here.

## Slide 7: Slow Start
Goal: reach knee quickly
Upon starting (or restarting) a connection
  cwnd =1
  ssthresh = adv_wnd
  Each time a segment is ACKed, cwnd++
Continues until…
  ssthresh is reached
  Or a packet is lost
Slow Start is not actually slow
  cwnd increases exponentially
Load
Goodput
Knee
Cliff

## Slide 8: Slow Start Example
1
2
3
4
5
6
7
cwnd = 1
cwnd = 2
cwnd = 4
cwnd = 8
cwnd grows rapidly
Slows down when…
  cwnd >= ssthresh
  Or a packet drops

## Slide 9: Congestion Avoidance
Additive Increase Multiplicative Decrease (AIMD) mode
ssthresh is lower-bound guess about location of the knee
If cwnd >= ssthresh then each time a segment is ACKed increment cwnd by 1/cwnd (cwnd += 1/cwnd).
So cwnd is increased by one only if all segments have been acknowledged

## Slide 10: Congestion Avoidance Example
Round Trip Times
cwnd (in segments)
Slow Start
cwnd >= ssthresh
cwnd = 1
cwnd = 2
cwnd = 4
cwnd = 8
cwnd = 9
ssthresh = 8

## Slide 11: The Big Picture – TCP Tahoe (the original TCP)
Time
cwnd
Timeout
Slow Start
Congestion
Avoidance
ssthresh

## Slide 12: Outline
UDP
TCP
Congestion Control
Evolution of TCP
Problems with TCP

## Slide 13: The Evolution of TCP
Thus far, we have discussed TCP Tahoe
  Original version of TCP
However, TCP was invented in 1974!
  Today, there are many variants of TCP
Early, popular variant: TCP Reno
  Tahoe features, plus…
  Fast retransmit
    3 duplicate ACKs? -> retransmit (don’t wait for RTO)
  Fast recovery
    On loss: set cwnd = cwnd/2 (ssthresh = new cwnd value)

## Slide 14: TCP Reno: Fast Retransmit
Problem: in Tahoe, if segment is lost, there is a long wait until the RTO
Reno: retransmit after 3 duplicate ACKs
1
2
3
4
5
6
7
cwnd = 1
cwnd = 2
cwnd = 4
2
3
4
4
4
4
3 Duplicate ACKs

## Slide 15: TCP Reno: Fast Recovery
After a fast-retransmit set cwnd to cwnd/2
  Also reset ssthresh to the new halved cwnd value
  i.e. don’t reset cwnd to 1
  Avoid unnecessary return to slow start
  Prevents expensive timeouts
But when RTO expires still do cwnd = 1
  Return to slow start, same as Tahoe
  Indicates packets aren’t being delivered at all
  i.e. congestion must be really bad

## Slide 16: Fast Retransmit and Fast Recovery
At steady state, cwnd oscillates around the optimal window size
TCP always forces packet drops
Time
cwnd
Timeout
Slow Start
Congestion Avoidance
Fast Retransmit/Recovery
ssthresh
Timeout

## Slide 17: Many TCP Variants…
Tahoe: the original
  Slow start with AIMD
  Dynamic RTO based on RTT estimate
Reno:
  fast retransmit (3 dupACKs)
  fast recovery (cwnd = cwnd/2 on loss)
NewReno: improved fast retransmit
  Each duplicate ACK triggers a retransmission
  Problem: >3 out-of-order packets causes pathological retransmissions
Vegas: delay-based congestion avoidance
And many, many, many more…

## Slide 18: TCP in the Real World
What are the most popular variants today?
  Key problem: TCP performs poorly on high bandwidth-delay product networks (like the modern Internet)
  Compound TCP (Windows)
    Based on Reno
    Uses two congestion windows: delay based and loss based
    Thus, it uses a compound congestion controller
  TCP CUBIC (Linux)
    Enhancement of BIC (Binary Increase Congestion Control)
    Window size controlled by cubic function
    Parameterized by the time T since the last dropped packet

## Slide 19: High Bandwidth-Delay Product
Key Problem: TCP performs poorly when
  The capacity of the network (bandwidth) is large
  The delay (RTT) of the network is large
  Or, when bandwidth * delay is large
    b * d = maximum amount of in-flight data in the network
    a.k.a. the bandwidth-delay product
Why does TCP perform poorly?
  Slow start and additive increase are slow to converge
  TCP is ACK clocked
    i.e. TCP can only react as quickly as ACKs are received
    Large RTT  ACKs are delayed  TCP is slow to react

## Slide 20: Goals
Fast window growth
  Slow start and additive increase are too slow when bandwidth is large
  Want to converge more quickly
Maintain fairness with other TCP varients
  Window growth cannot be too aggressive
Improve RTT fairness
  TCP Tahoe/Reno flows are not fair when RTTs vary widely
Simple implementation

## Slide 21: Compound TCP Implementation
Default TCP implementation in Windows
Key idea: split cwnd into two separate windows
  Traditional, loss-based window
  New, delay-based window
wnd = min(cwnd + dwnd, adv_wnd)
  cwnd is controlled by AIMD
  dwnd is the delay window
Rules for adjusting dwnd:
  If RTT is increasing, decrease dwnd (dwnd >= 0)
  If RTT is decreasing, increase dwnd
  Increase/decrease are proportional to the rate of change

## Slide 22: Compound TCP Example
Low
RTT
High
RTT
Aggressiveness corresponds to changes in RTT
Advantages: fast ramp up, more fair to flows with different RTTs
Disadvantage: must estimate RTT, which is very challenging
Time
cwnd
Timeout
Slow Start
Timeout
Slower cwnd growth
Faster cwnd growth

## Slide 23: TCP CUBIC Implementation
Default TCP implementation in Linux
Replace AIMD with cubic function
  B  a constant fraction for multiplicative increase
  T  time since last packet drop
  W_max  cwnd when last packet dropped

## Slide 24: TCP CUBIC Implementation
Default TCP implementation in Linux
Replace AIMD with cubic function
  B  a constant fraction for multiplicative increase
  T  time since last packet drop
  W_max  cwnd when last packet dropped

## Slide 25: TCP CUBIC Example
Less wasted bandwidth due to fast ramp up
Stable region and slow acceleration help maintain fairness
  Fast ramp up is more aggressive than additive increase
  To be fair to Tahoe/Reno, CUBIC needs to be less aggressive
Time
cwnd
Timeout
Slow Start
CUBIC Function
cwndmax
Fast ramp up
Stable
Region
Slowly accelerate to probe for bandwidth

## Slide 26: Outline
UDP
TCP
Congestion Control
Evolution of TCP
Problems with TCP

## Slide 27: Issues with TCP
The vast majority of Internet traffic is TCP
However, many issues with the protocol
  Poor performance with small flows
  Really poor performance on wireless networks
  Susceptibility to denial of service

## Slide 28: Small Flows
Problem: TCP is biased against short flows
  1 RTT wasted for connection setup (SYN, SYN/ACK)
  cwnd always starts at 1
Vast majority of Internet traffic is short flows
  Mostly HTTP transfers, <100KB
  Most TCP flows never leave slow start!
Proposed solutions (driven by Google):
  Increase initial cwnd to 10
  TCP Fast Open: use cryptographic hashes to identify receivers, eliminate the need for three-way handshake

## Slide 29: Wireless Networks
Problem: Tahoe and Reno assume loss = congestion
  True on the WAN, bit errors are very rare
  False on wireless, interference is very common
TCP throughput ~ 1/sqrt(drop rate)
  Even a few interference drops can kill performance
Possible solutions:
  Break layering, push data link info up to TCP
  Use delay-based congestion detection (TCP Vegas)
  Explicit congestion notification (ECN)

## Slide 30: Denial of Service
Problem: TCP connections require state
  Initial SYN allocates resources on the server
  State must persist for several minutes (RTO)
SYN flood: send enough SYNs to a server to allocate all memory/meltdown the kernel
Solution: SYN cookies
  Idea: don’t store initial state on the server
  Securely insert state into the SYN/ACK packet (sequence number field)
  Client will reflect the state back to the server

## Slide 31
Further topics

## Slide 32: Typical Internet Queuing
FIFO + drop-tail
  Simplest choice
  Used widely in the Internet
FIFO (first-in-first-out)
  Implies single class of traffic
Drop-tail
  Arriving packets get dropped when queue is full regardless of flow or importance
Important distinction:
  FIFO: scheduling discipline
  Drop-tail: drop policy

## Slide 33: RED Algorithm
Maintain running average of queue length
If avgq < minth do nothing
  Low queuing, send packets through
If avgq > maxth, drop packet
  Protection from misbehaving sources
Else mark packet in a manner proportional to queue length
  Notify sources of incipient congestion
  E.g. by ECN IP field or dropping packets with a given probability

## Slide 34: RED Operation
Min thresh
Max thresh
Average Queue Length
minth
maxth
maxP
1.0
Avg queue length
P(drop)

## Slide 35: RED Algorithm
Maintain running average of queue length
For each packet arrival
  Calculate average queue size (avg)
  If minth ≤ avgq < maxth
    Calculate probability Pa
    With probability Pa
      Mark the arriving packet: drop or set-up ECN
    Else if maxth ≤ avg
      Mark the arriving packet: drop, ECN

## Slide 36: Data Center TCP: DCTCP

## Slide 37: Generality of Partition/Aggregate
The foundation for many large-scale web applications.
  Web search, Social network composition, Ad selection, etc.
Example: Facebook
  Partition/Aggregate ~ Multiget
  Aggregators: Web Servers
  Workers: Memcached Servers
Memcached Servers
Internet
Web
Servers
Memcached Protocol

## Slide 38: Workloads
Partition/Aggregate
(Query)
Short messages [50KB-1MB]
(Coordination, Control state)
Large flows [1MB-50MB]
(Data update)
Delay-sensitive
Delay-sensitive
Throughput-sensitive
Notes: Replace PDF

## Slide 39: Impairments
Incast
Queue Buildup
Buffer Pressure

## Slide 40: Incast
TCP timeout
Worker 1
Worker 2
Worker 3
Worker 4
Aggregator
RTOmin = 300 ms
Synchronized mice collide.
  Caused by Partition/Aggregate.

## Slide 41: Queue Buildup
Sender 1
Sender 2
Receiver
Big flows buildup queues.
  Increased latency for short flows.
Measurements in Bing cluster
  For 90% packets: RTT < 1ms
  For 10% packets: 1ms < RTT < 15ms

## Slide 42: Data Center Transport Requirements
High Burst Tolerance
  Incast due to Partition/Aggregate is common.
Low Latency
  Short flows, queries
3. High Throughput
  Continuous data updates, large file transfers
The challenge is to achieve these three together.

## Slide 43: DCTCP: The TCP/ECN Control Loop
Sender 1
Sender 2
Receiver
ECN Mark (1 bit)
ECN = Explicit Congestion Notification
Notes: DCTCP is based on the existing Explicit Congestion Notification framework in TCP.

## Slide 44: DCTCP: Two Key Ideas
React in proportion to the extent of congestion, not its presence.
  Reduces variance in sending rates, lowering queuing requirements.
Mark based on instantaneous queue length.
  Fast feedback to better deal with bursts.
ECN Marks | TCP | DCTCP
1 0 1 1 1 1 0 1 1 1 | Cut window by 50% | Cut window by 40%
0 0 0 0 0 0 0 0 0 1 | Cut window by 50% | Cut window by 5%

## Slide 45: Data Center TCP Algorithm
Switch side:
  Mark packets when Queue Length > K.
  Sender side:
  Maintain running average of fraction of packets marked (α).
  In each RTT:
Adaptive window decreases:
  Note: decrease factor between 1 and 2.
B
K
Mark
Don’t
Mark
Notes: very simple marking mechanism
not all the tunings other aqms have
on the source side, the source is tryign to estimate the fraction of packets getting marked
using the obs that there is a stream of ecn marks coming back – more info in the stream than in any single bit
trying to maintain smooth rate variations to operate well even when using shallow buffers, and only a few flows (no stat mux)
F over the last RTT. In TCP there is always a way to get the next RTT from the window size. Comes from the self-clocking of TCP.
Only changing the decrease. Simplest version – makes a lot of sense. So generic could apply it to any algorithm – CTCP, CUBIC – how to cut its window leaving increase part to what it already does. Have to be careful here.