## Slide 1: Computer Networks
Practice 4 – traffic filtering, traffic analysis

## Slide 2: Overview
Examples of network protocols
Protocol Analysis
  Verify Correctness
  Analyze performance
  Better understanding of existing protocols
  Optimization and debugging of new protocols
Tools
  tcpdump & tshark
  Wireshark

## Slide 3: Network Protocol Examples
Defines the rules of exchange between a pair (or more) machines over a communication network
HTTP (Hypertext Transfer Protocol)
  Defines how web pages are fetched and sent across a network
TCP (Transmission Control Protocol)
  Provides reliable, in-order delivery of a stream of bytes
Your protocol here

## Slide 5: Protocol Analysis
Verify correctness
Debug/detect incorrect behavior
Analyze performance
Gain deeper understanding of existing protocols by “seeing” how they behave in actual use

## Slide 6: Analysis Methods
Instrument the code
  Difficult task, even for experienced network programmers
  Tedious and time consuming
Use available tools
  tcpdump / tshark
  Wireshark
  ipsumdump
Write your own tool
  libpcap

## Slide 7: Tools overview
Tcpdump
  Unix-based command-line tool used to intercept packets
    Including filtering to just the packets of interest
  Reads “live traffic” from interface specified using -i option …
  … or from a previously recorded trace file specified using -r option
    You create these when capturing live traffic using -w option
Tshark
  Tcpdump-like capture program that comes w/ Wireshark
  Very similar behavior & flags to tcpdump
Wireshark
  GUI for displaying tcpdump/tshark packet traces

## Slide 8: Tcpdump example
01:46:28.808262 IP danjo.CS.Berkeley.EDU.ssh > adsl-69-228-230-7.dsl.pltn13.pacbell.net.2481: . 2513546054:2513547434(1380) ack 1268355216 win 12816
01:46:28.808271 IP danjo.CS.Berkeley.EDU.ssh > adsl-69-228-230-7.dsl.pltn13.pacbell.net.2481: P 1380:2128(748) ack 1 win 12816
01:46:28.808276 IP danjo.CS.Berkeley.EDU.ssh > adsl-69-228-230-7.dsl.pltn13.pacbell.net.2481: . 2128:3508(1380) ack 1 win 12816
01:46:28.890021 IP adsl-69-228-230-7.dsl.pltn13.pacbell.net.2481 > danjo.CS.Berkeley.EDU.ssh: P 1:49(48) ack 1380 win 16560
Ran tcpdump
First few lines of the output:

## Slide 9: What does a line convey?
01:46:28.808262 IP danjo.CS.Berkeley.EDU.ssh >
adsl-69-228-230-7.dsl.pltn13.pacbell.net.2481: . 2513546054:2513547434(1380) ack 1268355216 win 12816
Timestamp
This is an IP packet
Source host name
Source port number (22)
Destination host name
Destination port number
TCP specific information
Different output formats for different packet types

## Slide 10: Similar Output from Tshark
1190003744.940437 61.184.241.230 -> 128.32.48.169 SSH Encrypted request packet len=48
1190003744.940916 128.32.48.169 -> 61.184.241.230 SSH Encrypted response packet len=48
1190003744.955764 61.184.241.230 -> 128.32.48.169 TCP 6943 > ssh [ACK] Seq=48 Ack=48 Win=65514 Len=0 TSV=445871583 TSER=632535493
1190003745.035678 61.184.241.230 -> 128.32.48.169 SSH Encrypted request packet len=48
1190003745.036004 128.32.48.169 -> 61.184.241.230 SSH Encrypted response packet len=48
1190003745.050970 61.184.241.230 -> 128.32.48.169 TCP 6943 > ssh [ACK] Seq=96 Ack=96 Win=65514 Len=0 TSV=445871583 TSER=632535502

## Slide 11: Demo 1 – Basic Run
Syntax:
tcpdump [options] [filter expression]
Run the following command
  tcpdump
Observe the output
Notes: Depending on the kind of traffic, make some general observations – sources, destinations, kinds of traffic, DNS requests etc. Too much of output.

## Slide 12: Filters
We are often not interested in all packets flowing through the network
Use filters to capture only packets of interest to us

## Slide 13: Demo 2
Capture only udp packets
  tcpdump “udp”
Capture only tcp packets
  tcpdump “tcp”

## Slide 14: Demo 2 (contd.)
Capture only UDP packets with destination port 53 (DNS requests)
  tcpdump “udp dst port 53”
Capture only UDP packets with source port 53 (DNS replies)
  tcpdump “udp src port 53”
Capture only UDP packets with source or destination port 53 (DNS requests and replies)
  tcpdump “udp port 53”

## Slide 15: Demo 2 (contd.)
Capture only packets destined to quasar.cs.berkeley.edu
  tcpdump “dst host quasar.cs.berkeley.edu”
Capture both DNS packets and TCP packets to/from quasar.cs.berkeley.edu
  tcpdump “(tcp and host quasar.cs.berkeley.edu) or udp port 53”
Notes: Ping quasar.cs.berkeley.edu.
Demonstrates the use of “or”

## Slide 16: How to write filters
Refer cheat sheet slides at the end of this presentation
Refer the tcpdump/tshark man page

## Slide 17: Running tcpdump
Requires superuser/administrator privileges on Unix
  http://www.tcpdump.org/
  You can do it on your own Unix machine
  You can install a Linux OS in Vmware on your machine
Tcpdump for Windows
  WinDump: http://www.winpcap.org/windump/
    Free software

## Slide 18: Wireshark System Overview

## Slide 19: Wireshark Interface

## Slide 20: Wireshark Interface

## Slide 21: Wireshark display filters
Display filters (also called post-filters) only filter the view of what you are seeing. All packets in the capture still exist in the trace
Display filters use their own format and are much more powerful then capture filters
Expressions can be interconnected with logical ops: or, and, xor, not.
Examples: tcp.flags.ack==1 and tcp.dstport==80

## Slide 22: Download
This document is basically a digest from “Wireshark User's Guide 25114 for Wireshark 1.0.0”
You can download the portable software
  http://www.wireshark.org/
http://wiki.wireshark.org

## Slide 23: Display Filter Examples
ip.src==10.1.11.00/24
ip.addr==192.168.1.10 && ip.addr==192.168.1.20
tcp.port==80 || tcp.port==3389
!(ip.addr==192.168.1.10 && ip.addr==192.168.1.20)
(ip.addr==192.168.1.10 && ip.addr==192.168.1.20) && (tcp.port==445 || tcp.port==139)
(ip.addr==192.168.1.10 && ip.addr==192.168.1.20) && (udp.port==67 || udp.port==68)
tcp.dstport == 80

## Slide 24: Assignment – sample2.pcap:
List the DNS queries in the pcap file? List the domain names to be resolved, and the resolved IP addresses of them!
What kind of traffic can be seen on the UDP port 53?
Determine the packets carrying http://lakis.web.elte.hu/results/nevsor0910II.pdf pdf file! Did the file successfully downloaded? What was the authorization string?
List the SNMP messages sent to 157.181.166.210!
What applications or protocols use UDP in the pcap file?
What is the content of the pdf file mentioned above?
Are there recursive DNS queries in the pcap?

## Slide 25: Assignment- sample3.pcap:
How many UDP packets are in the capture?
Determine the first http connection?
Show an example how an ordinary TCP connection is established and closed!
Determine the packets whose frame size is less than 100 bytes or equals to 618 bytes!
List the tcp traffic that uses port 49170!

## Slide 26: Assignment - HTTP
Download http_out.pcapng and answer the following questions (use WireShark):
  List the web pages downloaded! Which browser was used?
  How many images were downloaded? (hint: webp.)
  Are there encrypted communication in the file? (hint: SSL/TLS.) What can we say about encoded traffic?