## Slide 1: Computer Networks
Sándor Laki
ELTE-Ericsson Communication Networks Laboratory
ELTE FI – Department Of Information Systems
lakis@elte.hu
http://lakis.web.elte.hu
Based on the slides of Laurent Vanbever. Further inspiration: Scott Shenker & Jennifer Rexford & Phillipa Gill

## Slide 2: Last week on Computer Networks

## Slide 3: Overview
What is a network made of?

## Slide 4: Three main components
End-points
Switches
Links

## Slide 5: Overview
How to share network resources?

## Slide 6: Resource handling Two different approaches for sharing
Reservation
On-demand
Reserve the needed bandwidth in advance
Flow-level multiplexing
Send data when needed
Packet-level multiplexing

## Slide 7: Implementation
Packets
Packet-switching
e.g. Internet
Circuit-switching
e.g. landline phone networks
Reservation
On-demand

## Slide 8: Overview
How to organize the network?

## Slide 9
Access ISP
Access ISP
Tier-2 ISP
Tier-2 ISP
Tier-1 ISP
Tier-1 ISP
IXP

## Slide 10: This week
How does communication happen?
How do we characterize it?

## Slide 11: Briefly…
The Internet should allow
processes on different hosts
to exchange data
everything else is just commentary…

## Slide 12: Ok, but how to do that in a complex system like the Internet?

## Slide 13
Phone company
CabelTV company
University net
Enterprise net

## Slide 14
Alice
Bob
To exchange data, Alice and Bob use
a set of network protocols

## Slide 15: A protocol is like a conversational convention
The protocol defines the order and rules the parties should follow
Who should talk next and how to respond…
Alice
Bob
hello
hello
Give me http://elte.hu
Here it is…

## Slide 16: There are other kind of implementations…
Alice
Bob
hello
Give me http://elte.hu
Give me http://elte.hu
Give me http://elte.hu
Give me http://elte.hu
Give me http://elte.hu
Give me http://elte.hu
Gimme, gimme, gimme
a web site after Midnight

## Slide 17: Each protocol is governed by a specific API
Alice
Bob
while (…) {
message = …;
send(message, …);
}
while (…) {
message =receive(…);
}
WoW client
WoW server

## Slide 18: In practice, many existing protocols…
How does the Internet organize this???

## Slide 20: Modularity is a key component of any good system
can’t build large systems out of spaghetti code
hard (if not, impossible) to understand, debug, update
need to bound the scope of changes
evolve the system without rewriting it from scratch
Modularity is how we do it
…and understand the system at a higher-level
Problem
Solution

## Slide 21
„Modularity,
based on abstraction,
is the way things get done”
Barbara Liskov, MIT

## Slide 22: To provide structure to the design of network protocols, network designers organize protocols in layers
and the network hardware/software
that implement them

## Slide 23: Hálózatok modelljei
Internet rétegmodelljei
  TCP/IP modell: 4 réteget különböztet meg. 1982 márciusában az amerikai hadászati célú számítógépes hálózatok standardja lett. 1985-től népszerűsítették kereskedelmi felhasználásra. (Interop)
  Hibrid TCP/IP modell: 5 réteget különböztet meg (Tanenbaum, Stallings, Kurose, Forouzan)
Nyílt rendszerek hálózatának standard modellje
  Open System Interconnection Reference Model: Röviden OSI referencia modell, amely egy 7-rétegű standard, koncepcionális modellt definiál kommunikációs hálózatok belső funkcionalitásaihoz. (ISO/IEC 7498-1)

## Slide 24: TCP/IP modell (RFC 1122)
Alkalmazási réteg
(angolul Application layer)
Szállítói réteg
(angolul Transport layer)
Hálózati réteg
(angolul Internet layer)
Kapcsolati réteg
(angolul Link layer)
…
…
TELNET
FTP
DNS
HTTP
TCP
UDP
IP
ARPANET
SATNET
LAN
Ethernet
protokollok
hálózatok

## Slide 25: TCP/IP modell rétegei („bottom-up”)
Kapcsolati réteg / Host-to-network or Link layer
  nem specifikált
  a LAN-tól függ
Internet réteg / Internet or Network layer
  speciális csomagformátum
  útvonal meghatározás (routing)
  csomag továbbítás (angolul packet forwarding)
Szállítói réteg / Transport layer
  Transport Control Protocol
    megbízható, kétirányú bájt-folyam átviteli szolgáltatás
    szegmentálás, folyamfelügyelet, multiplexálás
  User Datagram Protocol
    nem megbízható átviteli szolgáltatás
    nincs folyamfelügyelet
Alkalmazási réteg / Application layer
  Szolgáltatások nyújtása: Telnet, FTP, SMTP, HTTP, NNTP, DNS, SSH, etc.

## Slide 26: Rétegek jellemzése
Szolgáltatás
  Mit csinál az adott réteg?
Interfész
  Hogyan férhetünk hozzá a réteghez?
Protokoll
  Hogyan implementáljuk a réteget?
Alkalmazási
Megjelenítési
Ülés
Szállítói
Hálózati
Adatkapcsolati
Fizikai

## Slide 27: Fizikai réteg
Szolgáltatás
  Információt visz át két fizikailag összekötött eszköz között
  definiálja az eszköz és a fizikai átviteli közeg kapcsolatát
Interfész
  Specifikálja egy bit átvitelét
Protokoll
  Egy bit kódolásának sémája
  Feszültség szintek
  Jelek időzítése
Példák: koaxiális kábel, optikai kábel, rádió frekvenciás adó
Alkalmazási
Megjelenítési
Ülés
Szállítói
Hálózati
Adatkapcsolati
Fizikai

## Slide 28: Adatkapcsolati réteg
Szolgáltatás
  Adatok keretekre tördelésezés: határok a csomagok között
  Közeghozzáférés vezérlés (MAC)
  Per-hop megbízhatóság és folyamvezérlés
Interfész
  Keret küldése két közös médiumra kötött eszköz között
Protokoll
  Fizikai címzés (pl. MAC address, IB address)
Példák: Ethernet, Wifi, InfiniBand
Alkalmazási
Megjelenítési
Ülés
Szállítói
Hálózati
Adatkapcsolati
Fizikai

## Slide 29: Hálózati réteg
Szolgáltatás
  Csomagtovábbítás
  Útvonalválasztás
  Csomag fragmentálás kezelése
  Csomag ütemezés
  Puffer kezelés
Interfész
  Csomag küldése egy adott végpontnak
Protokoll
  Globálisan egyedi címeket definiálása
  Routing táblák karbantartása
Példák: Internet Protocol (IPv4), IPv6
Alkalmazási
Megjelenítési
Ülés
Szállítói
Hálózati
Adatkapcsolati
Fizikai

## Slide 30: Szállítói réteg
Szolgáltatás
  Multiplexálás/demultiplexálás
  Torlódásvezérlés
  Megbízható, sorrendhelyes továbbítás
Interfész
  Üzenet küldése egy célállomásnak
Protokoll
  Port szám
  Megbízhatóság/Hiba javítás
  Folyamfelügyelet
Példa: UDP, TCP
Alkalmazási
Megjelenítési
Ülés
Szállítói
Hálózati
Adatkapcsolati
Fizikai

## Slide 31: Ülés v. Munkamenet réteg
Szolgáltatás
  kapcsolat menedzsment: felépítés, fenntarás és bontás
  munkamenet típusának meghatározása
  szinkronizációs pont menedzsment (checkpoint)
Interfész
  Attól függ…
Protokoll
  Token menedzsment
  Szinkronizációs checkpoints beszúrás
Példa: nincs
Alkalmazási
Megjelenítési
Ülés
Szállítói
Hálózati
Adatkapcsolati
Fizikai

## Slide 32: Megjelenítési réteg
Szolgáltatás
  Adatkonverzió különböző reprezentációk között
  Pl. big endian to little endian
  Pl. Ascii to Unicode
Interfész
  Attól függ…
Protokoll
  Adatformátumokat definiál
  Transzformációs szabályokat alkalmaz
Példa: nincs
Alkalmazási
Megjelenítési
Ülés
Szállítói
Hálózati
Adatkapcsolati
Fizikai

## Slide 33: Alkalmazási réteg
Szolgáltatás
  Bármi…
Interfész
  Bármi…
Protokoll
  Bármi…
Példa: kapcsold be a mobilod és nézd meg milyen appok vannak rajta…
Alkalmazási
Megjelenítési
Ülés
Szállítói
Hálózati
Adatkapcsolati
Fizikai

## Slide 34: ISO OSI modell
Az első 2-3 réteget minden eszköz implementálja
OSI: Open Systems Interconnect Model
Alkalmazási
Megjelenítési
Ülés
Szállítói
Hálózati
Adatkapcsolati
Fizikai
Hálózati
Adatkapcsolati
Application
Presentation
Session
Transport
Network
Data Link
Physical
Hoszt 1
Router/Switch
Hoszt 2
Fizikai
A rétegek peer-to-peer egymással kommunikálnak
A rétegek peer-to-peer egymással kommunikálnak

## Slide 35: Hybrid model – 5 layers
Each layer provides a service to the layer above
layer service provided
L5 Application high level network access
L4 Transport end-to-end delivery (reliable or not)
L3 Network global best-effort delivery
L2 Link local best-effort delivery
L1 Physical physical transfer of bits

## Slide 36: Each layer provides a service to the layer above by using the services of the layer directly below it
Applications
…built on…
Reliable (or unreliable) transport
…built on…
Best-effort global packet delivery
…built on…
Best-effort local packet delivery
…built on…
Physical transfer of bits

## Slide 37: Each layer has a unit of data (aka protocol data unit)
layer role (PDU)
L5 Application exchanges messages between processes
L4 Transport transports segments between end-systems
L3 Network moves packets around the network
L2 Link moves frames across a link
L1 Physical moves bits across a physical medium

## Slide 38: Each layer (except for L3) is implemented with different protocols
layer protocols
L5 Application HTTP, SMTP, FTP, SIP, …
L4 Transport TCP, UDP, SCTP
L3 Network IP
L2 Link Ethernet, Wifi, ADSL, WiMAX, LTE, …
L1 Physical Twisted pair, fiber, coaxial cable, …

## Slide 39: The Internet Protocol (IP) is the glue acting as a unifying network layer
layer protocols
L5 Application HTTP, SMTP, FTP, SIP, …
L4 Transport TCP, UDP, SCTP
L3 Network IP
L2 Link Ethernet, Wifi, ADSL, WiMAX, LTE, …
L1 Physical Twisted pair, fiber, coaxial cable, …

## Slide 40: Each layer is implemented with different protocols and technologies
layer technology
L5 Application
L4 Transport
L3 Network
L2 Link
L1 Physical
Software
Hardware

## Slide 41: Software and hardware advancements
Speed
Flexibility

## Slide 42: Software and hardware advancements
L1 L2 L3 L4 L5
Hardware
Software
programmable
network devices
highly optimized
libraries, drivers
SDN, P4
DPDK, FD.io, VPP

## Slide 43: Each layer takes messages from the layer above, and encapsulates with its own header and/or trailer
Application
Transport
Network
Link
HTTP
TCP
IP
Ethernet

## Slide 44
Application
Transport
Network
Link
HTTP
TCP
IP
Ethernet
HA
GET google.com
Header
Message

## Slide 45
Application
Transport
Network
Link
HTTP
TCP
IP
Ethernet
HA
GET google.com
Header
Message
HA
GET google.com
HT

## Slide 46
Application
Transport
Network
Link
HTTP
TCP
IP
Ethernet
HA
GET google.com
Header
Message
HA
GET google.com
HT
HA
GET google.com
HT
HN

## Slide 47
Application
Transport
Network
Link
HTTP
TCP
IP
Ethernet
HA
GET google.com
Header
Message
HA
GET google.com
HT
HA
GET google.com
HT
HN
HA
GET google.com
HT
HN
HE
TE

## Slide 48: In practice, layers are distributed on every network device
Application
Transport
Network
Link
HTTP
TCP
IP
Ethernet
HTTP
TCP
IP
Ethernet
IP
eth0
eth1
eth2
eth0
eth1
eth2

## Slide 49: Since when bits arrive they must make it to the application, all the layers exist on a host
Application
Transport
Network
Link
HTTP
TCP
IP
Ethernet
HTTP
TCP
IP
Ethernet
IP
eth0
eth1
eth2
eth0
eth1
eth2
hosts

## Slide 50: Routers act as L3 gateway as such they implement L2 and L3
Application
Transport
Network
Link
HTTP
TCP
IP
Ethernet
HTTP
TCP
IP
Ethernet
IP
eth0
eth1
eth2
eth0
eth1
eth2
Router
L3 Gateway

## Slide 51: Switches act as L2 gateway as such they only implement L2
Application
Transport
Network
Link
HTTP
TCP
IP
Ethernet
HTTP
TCP
IP
Ethernet
IP
eth0
eth1
eth2
eth0
eth1
eth2
Switch
L2 Gateway

## Slide 52: Wireshark demo

## Slide 53: Overview
How do we characterize the network?

## Slide 54: A network connection is characterized by its delay, loss rate and throughput
How long does it take for a packet to reach the destination
What fraction of packets sent to a destination are dropped?
At what rate is the destination receiving data from the source?
delay
throughput
loss

## Slide 55: Delay
delay

## Slide 56: Each packet suffers from several types of delays at each node along the path
transmission delay
+ propagation delay
+ processing delay
+ queueing delay
= total delay
due to link properties
due to traffic mix & switch internals

## Slide 57: Each packet suffers from several types of delays at each node along the path
transmission delay
+ propagation delay
+ processing delay
+ queueing delay
= total delay
tend to be tiny

## Slide 58
transmission propagation
propagation transmission
queuing queuing
processing processing
transmission
propagation

## Slide 59: The transmission delay is the amount of time required to push all of the bits onto the link
packet size [#bits] Transmission delay = [sec] link bandwidth [#bits/sec]
1000 bits Example = = 10 μsec 100 Mpbs

## Slide 60: The propagation delay is the amount of time required for a bit to travel to the end of the link
link length [m] Propagation delay = [sec] signal propagation speed [m/sec]
30000 m Example = = 150 μsec 2x108 m/sec (speed of light in fiber)

## Slide 61: How long does it take to exchange 100 Bytes packet?
Time
1 Mbps, 1 ms
Time to transmit
one bit = 10-6s
Time to transmit
800 bits = 800x10-6s
Time when that
bit reaches B:
10-6+10-3s
The last bit
reaches B at
(800x10-6)+10-3s
= 1.8ms

## Slide 62: If we have a 1 Gbps link, the total time decreases to 1.0008 ms
Time
1 Gbps, 1 ms
Time to transmit
one bit = 10-9s
Time to transmit
800 bits = 800x10-9s
Time when that
bit reaches B:
10-9+10-3s
The last bit
reaches B at
(800x10-9)+10-3s
= 1.0008 ms

## Slide 63: If we now exchange a 1GB file split in 100B packets
Time
1 Gbps, 1 ms
Time when that
bit reaches B:
10-9+10-3s
The last bit
reaches B at
(107x800x10-9)+10-3s
= 8001 ms
107 x 100B packets

## Slide 64: Different transmission characteristics imply different tradeoffs in terms of which delay dominates
107x100B pkts 1Gbps link transmission delay dominates
1x100B pkt 1Gbps link propagation delay dominates
1x100B pkt 1Mbps link both matter
In the Internet, we cannot know in advance which one matter!

## Slide 65: The queuing delay is the amount of time a packet waits (in a buffer) to be transmitted on a link
Queuing delay is the hardest to evaluate
as it varies from packet to packet
It is characterized with statistical measures
e.g., average delay & variance, probability of exceeding x

## Slide 66: Queuing delay depends on the traffic pattern

## Slide 73: Queues absorb transient bursts, but introduce queueing delays

## Slide 74: The time a packet has to sit in a buffer before being processed depends on the traffic pattern
Queueing delay depends on:
arrival rate at the queue
transmission rate of the outgoing link
traffic burstiness

## Slide 75
average packet arrival rate a [packet/sec]
transmission rate of outgoing link R [bit/sec]
fixed packets length L [bit]
average bits arrival rate La [bit/sec]
traffic intensity La/R

## Slide 76: When the traffic intensity is >1, the queue will increase without bound, and so does the queuing delay
Golden rule
Design your queuing system,
so that it operates far from that point

## Slide 77: When the traffic intensity is <=1, queueing delay depends on the burst size

## Slide 78: Loss
loss

## Slide 79: In practice, queues are not infinite. There is an upper bound on queuing delay.

## Slide 80: If the queue is persistently overloaded, it will eventually drop packets (loss)

## Slide 81: Throughput
throughput

## Slide 82: The throughput is the instantaneous rate at which a host receives data
data size [#bits]
Average throughput =
[#bits/sec] transfer time [sec]

## Slide 83: To compute throughput, one has to consider the bottleneck link

## Slide 84: To compute throughput, one has to consider the bottleneck link… and the intervening traffic

## Slide 85: As technology improves, throughput increase & delays are getting lower except for propagation (speed of light)

## Slide 86: Because of propagation delays, Content Delivery Networks move content closer to you
* http://wwwnui.akamai.com/gnet/globe/index.html

## Slide 87: Brief history of Internet

## Slide 88: The Internet history starts in the late 50’s…
Phone networks = the communication network
fully circuit-switched
People wanted to use networks for other things
defense, computers, etc.
circuit-switching does not fit to these new requirements…
inefficient for bursty loads and not resilient

## Slide 89: Three main questions
How can we design a more resilient network?
… led to the invention of packet switching
How can we design a more efficient network?
… also led to the invention of packet switching
How can we connect all these networks together?
… the invention of Internet as we know it
Paul Baran RAND
Leonard Kleinrock UCLA
Vint Cerf & Bob Kahn
DARPA

## Slide 90: The 60’s was all about packet switching…
Advanced Research Projects Agency NETwork (ARPANET)
UCSB
SRI
UCLA
UTAH
STAN
SCD
RAND
BBN
ILLINOIS
MIT
LINCOLN
HARVARD
BURROUGHS
CRAN
CASE
1969 december
1970 july
1971 march

## Slide 91: ARPANET
April 1972

## Slide 92: ARPANET
September 1972

## Slide 93: ARPANET

## Slide 94: The first message over the Internet
29. Oct. 1969 Leonard Kleinrock from UCLA tries to log in a Stanford computer
UCLA
Stanford
We typed the L… Do you see it?
Yes! We see the L
We typed the O… Do you see it?
Yes! We see the O
We typed the G.
… and the system crashed …
* http://ftp.cs.ucla.edu/csd/first_words.html
: „LO”

## Slide 95: The 70’s about Ethernet, TCP/IP and email…
1971 Network Control Program (NCP)
Predecessor of TCP/IP
1972 Email and Telnet
1973 Ethernet
1974 TCP/IP
Paper of Vint Cerf and Bob Kahn

## Slide 96: 80’s when TCP/IP went mainstream
1983 NCP to TCP/IP
Domain Name Service (DNS)
1985 NSFNet (TCP/IP)
198x First Internet crashes caused by congestion
1986 Van Jacobson saves the Internet
congestion control

## Slide 97
Van Jacobson

## Slide 98: 90’s – the Internet going commercial…
1989 ARPANET closed
Birth of the WEB
Tim Berners Lee (CERN)
1993 First search engine (Excite)
1995 NSFNet closed
1998 Google reinvents searching

## Slide 99: The new millenium bringing Web 2.0
1998 IPv6 standardization
2004 Facebook goes online
2006 Google buys YouTube
2007 Netflix strats streaming videos
2007 First iPhone with mobile Internet access

## Slide 100: Fast Internet access everywhere, every device needs an Internet connection
2009 Mining of the Bitcoin genesis block
Fast mobile Internet access: 4G/LTE
IoT boom
Internet of Everything
2018 Only 26% of Alexa Top 1000 sites reachable over IPv6
Soon? Encrypted transport protocols
For example QUIC
Ultra-fast mobile access – 5G

## Slide 101: Standardization of Internet protcols
https://twitter.com/biellacoleman/status/1021138393252712449?lang=en
They uses collective humming to get consesus for technical discussions…

## Slide 102: To be continued…