## Slide 2
Where’s WikiLeaks?

## Slide 6: Spotter:
GEOLOCATION SERVICE
Sándor Laki*
Eötvös Loránd University
Budapest, Hungary
lakis@inf.elte.hu
A Model Based Active Geolocation Service
S. Laki*, P. Mátray, P. Hága, T. Sebők, I. Csabai, G. Vattay
The Project was supported by the European Union and co-financed by the European Social Fund (grant agreement no. TAMOP 4.2.1./B-09/1/KMR-2010-0003).

## Slide 7: Motivation
Location information can be useful for both private and corporate users
  Targeted advertising on the web
  Restricted content delivery
  Location-based security check
Scientific applications
  Measurement visualization
  Network diagnostics
  Analysing spatial properties
  of the Intenet

## Slide 8: IP Geolocation in general
Passive Geolocation
Geolinguistic
Registry based
  Whois, dns
  Organizational infromation
Commercial databases
  Maxmind, IPLigence, IP2Location, etc.
Active Geolocation
rt1.lon.uk.geant2.net
London, UK

## Slide 9: IP Geolocation in general
Geolinguistic
Registry based
  Whois, dns
  Organizational infromation
Commercial databases
  Maxmind, IPLigence, IP2Location, etc.
rt1.lon.uk.geant2.net
Passive Geolocation
Active Geolocation
Large and geographically dispersed IP blocks can be allocated to a single entity

## Slide 10: IP Geolocation in general
Geolinguistic
Registry based
  Whois, dns
  Organizational infromation
Commercial databases
  Maxmind, IPLigence, IP2Location, etc.
rt1.lon.uk.geant2.net
Passive Geolocation
Active Geolocation
Active probing
  Delay, topology, etc.
Landmarks
  With known location
Location estimates for each individual IP addresses
Large and geographically dispersed IP blocks can be allocated to a single entity

## Slide 11: Active geolocation
?
Target
to be localized

## Slide 12: Active geolocation
Landmarks with known location

## Slide 13: Active geolocation
200 ms
1010 ms
898 ms
501 ms

## Slide 14: Active geolocation
Transforming delays to geographical distances

## Slide 15
How to transform network delays to geographical distances?

## Slide 16: Our delay–distance model
Reference data set
Nodes with known location
~700 PlanetLab nodes
All to all RTT measurements
  mininmum delays

## Slide 17: Our delay-distance model
Standardized values, fitted normal distribution
Approximated by a standard normal distribution
Geographic distances follow normal distribution
  with parameters µ(t) and (t) for a given delay t

## Slide 18: Evaluation
The distances are normally distributed for a given RTT
For each RTT the radial profile is approximated by a normal distribution (m(d) and s(d)) => which defines the spatial probability distribution of the target

## Slide 19: Evaluation – „Triangulation”
Landmarks: L1, … , Ln
Delay di from Li to T: Li di
The probability that target T resides in region H:

## Slide 20: Performance analysis
Estimated accuracy for a geolocation ground truth
  CAIDA’s Geolocation Comparision Survey
  More than 20000 reference nodes
    Located in North America and in Europe
In North America
35%
9%
2%
70%
40%
27%

## Slide 21: The Online service

## Slide 22: Spotter - The geolocation service
online: free, easy to use
  ~100 landmarks
  Real time measurements in the background
offline: batch mode
  ~50k addresses/day
  Full landmark set
    ~700 nodes
to fix:
  DNS resolve problem
  Sequential queuing
visit and use! http://spotter.etomic.org

## Slide 23
Where’s WikiLeaks?

## Slide 24: Conclusion
Spotter is a measurement based geolocation service available online
Based on a probabilistic approach
  A novel description of delay-distance relation
Validated on CAIDA’s Geolocation Ground Truth
  30 km and 75 km median accuracy in North America and in Europe, resp.
New challenges:
  IPv6, Real time measurements, etc
  The Internet topology and the delay characteristics could be changed in the future

## Slide 25
Thank you for your attention!
For more info please visit
http://spotter.etomic.org
or send me an email
lakis@inf.elte.hu (Sándor Laki)
GEOLOCATION SERVICE